M365 Admin module Installation

To properly install the M365Admin, the files need to be published to a PowerShell repository. The repository needs to be accessible to all servers. PSGallery is common open repository.
  Since this module is not published on PSGallery there is an alternative manual method to install this module. It is unsupported and not recommended.
The ZIP file folder contains the files organized for use as a module, including the module version number folder.
  Modules are installed in the $env:PSModulePath folders:
#1:
C:\Users\<USERNAME>\Documents\WindowsPowerShell\Modules
or
C:
  Users
    <USERNAME>
      Documents
        WindowsPowerShell
        Modules
#2:
C:\Program Files\WindowsPowerShell\Modules
or
C:
  Program Files
    WindowsPowerShell
      Modules

The #1 location is the current user’s profile folder PowerShell module path. You do not need local administrators right to add a module to this location. The module will only be available to you, or anyone else that extracted the ZIP to their respective path (their profile folder).
Extract the ZIP folder at this location. The folder structure should look like:
C:\Users\<USERNAME>\Documents\WindowsPowerShell\Modules\M365Admin\1.0.0\
or
C:
  Users
    <USERNAME>
      Documents
        WindowsPowerShell
        Modules
        M365Admin
        1.0.0 [whatever current module version number]
        En-US
        Public
        Test

You can test the installation from a PowerShell console by entering:
Get-Module -Name M365Admin -ListAvailable
   Directory: C:\Users\<USERNAME>\Documents\WindowsPowerShell\Modules
ModuleType Version Name ExportedCommands
---------- ------- ---- ----------------
Script 1.0.0 M365Admin {Connect-M365Admin, Conv...

The #2 location is the Windows system PowerShell module path. You will need local administrators right to add a module to this location. The module will be available to everyone.
Extract the ZIP folder at this location. The folder structure should look like:
C:\Program Files\WindowsPowerShell\Modules\M365Admin\1.0.0\
or
C:
  Program Files
    WindowsPowerShell
      Modules
        M365Admin
        1.0.0 [whatever current module version number]
        En-US
        Public
        Test

You can test the installation from a PowerShell console by entering:
Get-Module -Name M365Admin -ListAvailable
   Directory: C:\Program Files\WindowsPowerShell\Modules
ModuleType Version Name ExportedCommands
---------- ------- ---- ----------------
Script 1.0.0 M365Admin {Connect-M365Admin, Conv...